## Slide 1: ENGI 301 Tank Refillerator PCB
11/19/18
Adulfo Amador

## Slide 2: Background Information
As a result of the mostly successful midterm project, I decided to create a PCB attachment for the PocketBeagle that would allow for all the external pieces to be connected to one small board. This will include attachments for the temperature probe, the motor, and the button/limit switch. Additionally, the board will be able to house the OLED display as well. Much like the functionality of my Tank Refillerator midterm, the board will have input for all of the items mentioned previously. This will allow for saving space as well as create a more compact model. The board will be able to be unpressed/pressed to allow water flow or not through the use a transistor and a diode. Additionally, for future project additions there will be inputs for an ultrasonic sensor that will possibly be used later in the progression of the project.

## Slide 3
PocketBeagle
SPI0
ClickBoard 1 Position
GPIO
USB0
5 Volts
System Block Diagram
OLED Screen
GPIO
GPIO
GPIO
GPIO
PIN 110: Transistor
PIN 117: Limit Switch
PIN 45: Temperature Probe
PIN 88: Ultrasonic Sensor
PIN 111: Emergency Stop Button

## Slide 4
3.3 Volts
5 Volts
PocketBeagle
SYS_RTC_1P8V
VDDSHV1
SYS_VDD3_3P3V
VIN_USB
SYS_VDD_1P8V
SYS_VDD1_3P3V
VIN_AC
3.3V Components
(up to 500 mA)
VDDSHV2
VDDSHV3
VDDSHV4
VDDSHV5
VDDSHV6
OLED display
Temp Probe
3.3V or 1.8V Connections
Power Block Diagram
Motor
Transistor
Button/Limit Switch
Emergency Stop Button

## Slide 5
Tank PCB
Power Block Diagram
56mm
35mm
Auxiliary Motor Connector
Auxiliary Temperature Connector
Auxiliary Ultrasonic Sensor Connector
Auxiliary Button Hub (accepts up to 3 buttons/limit switches)
Click OLED Screen Plugin
Barrel Jack (Power)
Emergency Stop Button
Auxiliary Connectors will be of the through hole type JST.